## Slide 1: IoT Security Enhancement using Physical Layer signatures
PROJECT GUIDE : MRS. N. VIJAYA
NARAYANAN B - 2016105053
VENKAT KRISHNAN B K J - 2016105077
ASHOK KUMAR M - 2016105513

## Slide 2: INTRODUCTION
Wireless networks are susceptible to various attacks due to the “open air” nature of the wireless communication
A secure wireless communication system involves authentication and secure transmission
  Authentication verifies the user identity and prevents malicious users from accessing the network
  Secure transmission protects data integrity and confidentiality using encryption schemes
IoT Security
  Devices are low powered and mostly battery operated
  Flawed because of the operational limitations on the computational power
Physical layer signatures
  Fine-grained values derived from the physical layer, such as RSS and CSI.
  Very sensitive to location and time
  Presents an excellent quality of randomness

## Slide 3: Various factors affecting the signal
Channel Model

## Slide 4: MOTIVATION
Drawbacks of Conventional Cryptography Techniques
Due to the “open-air” nature, key distribution is more susceptible to attacks in wireless communications.
Mathematically Complex in the case of IoT devices
Physical Layer Security
It involves physical layer signatures which are very random, unique and doesn’t involves complex mathematical computations
Physical Layer Security + Cryptographic Techniques
Existing cryptographic securities can be enhanced with the incorporation of physical layer signatures

## Slide 5: Existing Method Proposed Method

## Slide 6: OBJECTIVE
To develop a new secret key generation algorithm using physical layer signatures (Channel State Information).
To overcome key exchange, key distribution and key management overhead at legitimate users.
To provide significant improvement in secrecy.

## Slide 7: METHODOLOGY
MAC
Hash
E
||
D
MAC
Hash
E
CSI
CSI
K
K
Verification
Authenticated User
Yes
E
K
K
 | Encryption
K | Key
 | Decryption
E
D

## Slide 8: FLOWCHART
QUANTIZATION
CSI EXTRACTION
PRIVACY AMPLIFICATION
SHA - 256
K
Ku
Si

## Slide 9: QUANTIZATION ALGORITHM
INPUT: Absolute value of CSI, of length ,
OUTPUT:
Step 1: To find and of
Step 2: To find quantization threshold by using
Step 3: Compare with
if then
else if then
Step 4:

## Slide 10
Step 5: while
if
if
Compare with
if then
else if then
Step 6:

## Slide 11: ENCRYPTION
This encryption technique is based on the constellation rotation in modulation techniques which enhances the security provided in the above layers.
The constellation rotation requires a phase value to be calculated from the generated key.
Every constellation symbol Sk is rotated by a unique angle α as
where, - Original constellation symbol
- Rotated constellation of

## Slide 12: PHASE CALCULATION
To generate an unique angle with respect to the generated key.
The 256 bit key is split into 8 bit words to find 32 phases.
 | Bits used to determine the quadrant of the phase
 | Sign Bits
 | Magnitude Bits

## Slide 13: QUADRANT BITS
The first two bits in the 8 bit word are used to determine the quadrant of the required phase.
The bits are converted to it’s decimal equivalent i.
The base angle is determined by
a1 | a2
b | 
SIGN BIT
If b is 0, the constellation is rotated in the anticlockwise direction.
If b is 1, the constellation is rotated in the clockwise direction.

## Slide 14: MAGNITUDE BITS
These 5 bits are used to determine the position in the respective quadrant.
The decimal equivalent is determined as n and the required magnitude can be equated as
Now, the unique angle is determined from the 8-bit word as
C1 | C2 | C3 | C4 | C5

## Slide 15: DECRYPTION
The original constellation symbol can be recovered as
where, - Original constellation symbol
- Rotated constellation of
The angle α is unique for every user as the CSI is unique. The resulting α varies even between the 32 words that makes the constellation rotation more random and more secure.

## Slide 16: PERFORMANCE METRICS
MISMATCH RATE
Mismatch rate is defined to be ratio of mismatched bits between the secret keys independently generated by the user and the provider.
In the coherence time interval, the mismatch rate is ideally zero between the sender and receiver, but practically due to noise, distortion etc., it is a very low value.
LEAKAGE RATE
Leakage measures the amount of information learned by the adversary.
Leakage is defined to be the ratio of matched bits between the sender and the adversary. An encryption scheme with lower leakage is more secure.

## Slide 17: PERFORMANCE METRICS
BER PERFORMANCE
The bit error ratio (also BER) is the number of bit errors divided by the total number of transferred bits during a time interval.
The evaluations show that the bit error decreases with an increase in SNR for the intended user but the bit error remains constant even with an increase in SNR for the adversary.
KEY VARIATION WITH TIME
The CSI is generally very sensitive to variations with time. The key generated by the different users at different time intervals even at the same location are hence unique and random.
A higher key variation will result in better security.

## Slide 18: RESULTS
Data extracted from NIC
Sample CSI data

## Slide 19
CSI Samples varying with respect to distance and time

## Slide 20
Keys generated for different CSI values

## Slide 23: PERFORMANCE METRICS
LEAKAGE RATE

## Slide 24: BER PERFORMANCE OF DIFFERENT MODULATION SCHEMES
QAM-16

## Slide 25: BER PERFORMANCE OF DIFFERENT MODULATION SCHEMES
QAM-32

## Slide 26: BER PERFORMANCE OF DIFFERENT MODULATION SCHEMES
QAM-64

## Slide 27: KEY VARIATION WITH TIME

## Slide 28: REFERENCES
Physical Layer Security for the Internet of Things by Junqing Zhang, Sekhar Rajendran, Zhi Sun, Member, IEEE, Roger Woods, Senior Member, IEEE, and Lajos Hanzo, Fellow, IEEE. Published in: IEEE Wireless Communications (Volume:26, Issue: 5, October 2019)
Key Generation From Wireless Channels: A Review by Junqing Zhang, Trung Q. Duong, (Senior Member, IEEE), Alan Marshall, (Senior Member, IEEE), and Roger Woods, (Senior Member, IEEE) 2016. Published in: IEEE Access (Vol. 4)
Wireless Physical Layer Identiﬁcation : Modeling and Validation, by W.Wang, Z.Sun, S. Piao, B. Zhu, and K. Ren, IEEE Trans. Inf. Forensics Security, vol. 11, no. 9, pp. 2091–2106, 2016
Efﬁcient and Secure Key Extraction using CSI without Chasing down Errors
Jizhong Zhao, Wei Xi, Jinsong Han, Shaojie Tang, Xiangyang Li, Yunhao Liu, Yihong Gong, Zehua Zhou